137/12 					 				 	     3142

4-HIGH PRECISION LEVELLER

Manufacturer: WMW-UBR

Model: UBR 01-C 3x1600

Material thickness: .7-4.0mm (Rm = 420 N/mm2)

Material width max: 1.600mm

N. of work rolls: 21

Diameter of work rolls: 60 mm / Roll length: 1.720mm

Back-up roll sets: 3+3

Back-up rolls are adjustable by means of electric 3-phase motors

Working speed : 15 m/’ with 1600 rpm motor

Tilting movement: by electric motor

Screwdown movement: by two electric motors, independent for each side

Lubrication system: automatic, with electric oil pump for pinion stand

Grease pump on work rolls bearings

Condition: good; however we offer:

OPTION 1:  machine as is, where is * ( * warehoused at our PLANT 2 )

OPTION 2:  machine full-revamped

Excluding: main motor, electric cabinet.