183/12

SLITTING LINE     400mm x 2,5 mm

Manufacturer: OCMER (Italy)

Max coil width: 400mm

Thickness min-max: 0,5 – 2,5mm (Rm = 400 N/mm2) / 1,8mm (Rm = 650 N/mm2)

Max coil weight: 1,5 t

Coil I.D. at entry: 400-500 mm (with spacers)

Slit coil I.D. at recoiling: 410

Speed: max 100 m/min

Direction: right to left

Description:

- Decoiler:

Pneumatic expansion, idler

Mandrel expansion range: 390mm to 425mm (with spacers for also 500mm I.D.)

Snubber arm

- Slitter Head with shaft dia.: 80mm

AC motor drive with adjustable speed (Inverter)

- Scrap Baler, single drum type – 400mm x 400mm

- Loop Roll Tables  (NEW)

- Felt press (strip Tension Stand) with 2 (NEW) Separator Rolls

- Recoiler, with separator arm and ejection plate

Max coil O.D.: 1.350 mm    -- AC motor, adjustable speed (Inverter)

Slit Coil I.D.: 410mm

- Turnstile

- Electric cabinet, operator switchboard (NEW)

- Set of knifes, separating disk, rubber disk, spacers….

Condition: carefully revamped, ready for delivery